# Notes supervision check_mk
Voir :
- https://en.wikipedia.org/wiki/Check_MK
- https://www.min2rien.fr/wp-content/uploads/2014/02/Nicolas_Jamin_13022014_Supervision.pdf
Voir aussi : Nagios, Centreon, Shinken
Note : si vous n'avez pas encore choisi de solution de supervision, Pensez à regarder Zabbix.
## Install de check_mk sur Debian
apt-get install xinetd check-mk-agent

n'oublier pas de modifier la ligne disable = yes /etc/xinetd.d/check_mk
service check_mk
{
        type = UNLISTED
        port = 6556
        socket_type = stream
        protocol = tcp
        wait = no
        user = root
        server = /usr/bin/check_mk_agent
        # If you use fully redundant monitoring and poll the client
        # from more then one monitoring servers in parallel you might
        # want to use the agent cache wrapper:
        #server = /usr/bin/check_mk_caching_agent
        # configure the IP address(es) of your Nagios server here:
        #only_from = 127.0.0.1 10.0.20.1 10.0.20.2
        # Don't be too verbose. Don't log every check. This might be
        # commented out for debugging. If this option is commented out
        # the default options will be used for this service.
        log_on_success =
        #disable = yes
        disable = no
}
systemctl restart xinetd

lsof -i TCP:6556 nc 127.0.0.1 6556